## Slide 1: Inside a Clunker Computer
Andrea Slaven
TED 501 Spring 2013

## Slide 2: Model:
Dell Optiplex 170L
Mini-Tower

## Slide 3: Back of Unit

## Slide 4: Back of Unit
Power supply
parallel connector
mouse connector
network adapter connector
serial connector
video connector
keyboard connector
USB 2.0 connectors (4)
line-in connector
line-out connector
microphone connector

## Slide 5: Opening the Case
A lever is on the back of the case. Push towards bottom to release.

## Slide 6
Lift the side and take the cover off.

## Slide 7: Insides of the Computer
CD drive
secondary CD bay
floppy drive
hard drive
secondary hard drive bay
power supply
system board
Protective cover
over processor

## Slide 8: Unplug power
P-9 cord to the CD drive
P-3 cord to the hard drive
1
2

## Slide 9: Unplug power
P-7 cord to the floppy drive
P-1 cord to the motherboard
3
4

## Slide 10: Unplug power
P-2 cord to the processor power connector (J5B1)
Front-panel audio connector
5
6

## Slide 11: Unplug power
Front-panel connector (J9G1)
7
8
Front-panel USB connector (J9G1)

## Slide 12: Unplug power
CPU Fan Connection
9

## Slide 13: Unplug Data Cables
Cable to CD drive
Cable to Floppy drive
Cable to Hard Drive

## Slide 14: Remove Fan
Remove the four screws that secure the power supply to the back of the computer. wqê
Remove the power supply from the computer.

## Slide 15: Remove Hard Drive
Remove the hard drive-securing screw, and then remove the hard drive from the bracket.
Remove the two bracket-securing screws, and
then remove the drive bracket from the computer.

## Slide 16: Front Panel Drives…
In order to get to the CD Drive and the Floppy Drive, the front panel needs to be removed.
This was done by releasing the top latch, and a bottom latch found at the bottom of the inner wall.
Once the latches were released, the front panel was able to come off.
o
latches

## Slide 17: Removing CD Drive
Remove screw from bracket.
Slide CD drive out from front.

## Slide 18: Removing Floppy Drive
Remove screw to release bracket from case.
Remove screws to release Floppy drive out from front.

## Slide 19: The Motherboard (Mobo)
DIMM Cards in slots
Heat sink
CPU
battery
Expansion Slots
Power connector
floppy drive connector
hard-drive connector
CD/DVD drive
Chip Set

## Slide 20: More Mobo
Removing a DIMM Card
DIMM Cards
Press down on levers to release DIMM card.
Lift DIMM card up.

## Slide 21: More Mobo
This CMOS uses jumper settings.

## Slide 22: CPU, CPU, Where are you?
First I removed the green clips that locks the heat sink to the retention base. Next, to remove the heat sink, press the tabs on the retention base while lifting one end of the heat sink
The CPU socket is now
exposed…but where is
the CPU?
If there was a CPU, it would be sitting ontop of the socket. To remove it, lifting the lever releases it

## Slide 23: Putting it all back together!
This was just a matter of going backwards.
The CPU heat sink was locked into place.
Floppy Drive was replaced with 4 its screws.
The CD Drive was slid back into its housing and screwed in place.
The front of the case was replaced simply by lining it up, and pressed into place until it clicked.
Then the hard drive was replaced into its bracket, and place back with its screws.

## Slide 24: Putting it all back together!
Plugging in the cables and the power.
First, I reconnected the data cables: Hard drive, CD drive and Floppy Drive.
Next, returned the power supply by lining it back in place and securing it with 4 screws.
Next, power went to CPU Fan, the processor power, Mother Board, CD Drive, Floppy
Drive, Front panel and USB connections.
The cover was closed over the processor.

## Slide 25: Done! That was Fun!
The side panel was then slid back in place.
This unit had simple hardware that used a Philip’s head screwdriver.
Also used was a needle nose, just to help when my fingers could not hold small screws.
The brush was used to remove dust.
Normally, an anti-static bracelet would be worn, but this unit has not had
power in it for a long time.